## Slide 1: IP Lookup Implement
Speaker: Hung-You Chen
Advisor Professor: Pi-Chung Wang
Date: 2022/01/18

## Slide 2: Outline
Introduction
Related Work
Scheme
Result
Conclusion

## Slide 3: Introduction
IP lookup is a task of routing performing that checking the routing table in order to find the most matched prefix of IP Address.
It is the longest match prefix in the routing table.
It always cares about memory access times and memory storage.
In the class, It has been introduced many algorithms to perform this task.
I decide to use Radix Trie to implement IP lookup with C.

## Slide 4: Related Work

## Slide 5: Scheme
Radix Trie algorithm
1. Prepare an array of struct to save the index and the binary-form and the length of prefixes.
(1) struct prefix_info {
int index;
int len;
char Bstring[32];
};
prefix_info* prefixes = malloc(1000000* sizeof *prefixes);
2. Insert every index of prefix into binary tree.
(1) insert(&root, prefixes[i], 0) //0 means level
3. Binary Search Tree to find the lonest prefix of the target IP Address.
(1) search(&root, target IP, 0) //0 means level

## Slide 7: Result
rrc00’s “prefix_20211122.txt” to be as routing table
rrc00’s “trace_20211122.txt” to be as target IPs
It takes about 9.028 seconds to find the longest prefix of about 9M target IPs.

## Slide 8: Conclusion
It is O(W) time complexity. W=bits
It takes about 40 x 900000 bytes=(34.3M) to save routing table information.
Max memory access times:32
Average memory access times =